## Slide 1: Extending MSFS with hardware cockpit components
Minimal code for a single ON/OFF switch
(not a HID device based solution)
Gábor Hraskó
December 2020

## Slide 2: ON-OFF switch for controlling Radio Master switch in MSFS 2020
Arduino program (C++) in Arduino IDE
Python 3.5+ program on the PC
(pyserial and fsuipc libs)
FSUIPC 7
(free version)
MSFS 2020
Arduino compatible card
Windows 10 PC

## Slide 3: Arduino UNO compatible board with a single ON-OFF switch
ON-OFF switch connections:
GND
Digital pin 2
GND
Pin 2

## Slide 4: C++ program for the board developped and deployed in Arduino IDE
#define BAUDRATE 9600
#define DELAY 100
#define PIN 2
#define PIN 13
bool SwitchIsOn;
// put your setup code here, to run once:
void setup() {
Serial.begin( BAUDRATE ); // Initialize serial (USB) communication
pinMode(PIN, INPUT); // Define pin as input for the toggle switch
digitalWrite(PIN, HIGH); // Enable pull-up resistor on pin
SwitchIsOn = (digitalRead(PIN) == LOW); // Get initial state. ON is 0V due to pull-up configuration
Serial.println( SwitchIsOn ? "1" : "0");
}
// put your main code here, to run repeatedly:
void loop() {
bool ActSwitchIsOn = (digitalRead(PIN) == LOW); // Get current state
if( ActSwitchIsOn != SwitchIsOn ) // Switch state has changed
{
SwitchIsOn = ActSwitchIsOn;
Serial.println( SwitchIsOn ? "ON" : "OFF"); // Sending the state via USB (COM)
digitalWrite(LEDPIN, SwitchIsOn ? HIGH : LOW); // Display status on the on-board LED
}
delay( DELAY );
}
You might have to download and install the Windows driver of the board. For my SparkFun RedBoard Qwiic the driver can be found here: https://learn.sparkfun.com/tutorials/how-to-install-ch340-drivers
The COM port number for the USB connection can be found in Windows Device Manager / Ports and it is also displayed at the bottom-left corner of the Arduino IDE window.

## Slide 5: Python 3 program as USB – FSUIPC connector on the PC
C:\> cd \venvs
C:\venvs> py -m venv msfs
C:\venvs> cd msfs
C:\venvs\msfs> Scripts\activate
(msfs) C:\venvs\msfs> python -m pip install --upgrade pip
(msfs) C:\venvs\msfs> pip install pyserial
(msfs) C:\venvs\msfs> pip install fsuipc
import serial # USB serial communication
from fsuipc import FSUIPC # FSUIPC communication
# USB (COM) port configuration
serial_port = 'COM7'
baud_rate = 9600
arduino = serial.Serial(serial_port, baud_rate, timeout=0.1)
with FSUIPC() as fsuipc:
# Prepare data structure for sending through FSUIPC
prepared = fsuipc.prepare_data([
(0X3103, "b")
], False)
# Monitoring COM port and sending received data to FSUIPC. Also logging to terminal
while True:
data = arduino.readline().decode("ascii")[:-2] # Dropping new-line chars
if data == 'ON':
print('->ON')
prepared.write( [1] )
elif data == 'OFF':
print('->OFF')
prepared.write( [0] )
Comments:
Setting up python virtual environment with the two required libs
Card is connected via COM7
FSUIPC offset of avionics switch is 0x3103, type is 8 bit unsigned
FSUIPC functions expect array inputs even if we have a single value, so we pass the parameters as a 1-member arrays
Logging to stdio

## Slide 6: Connecting to MS Flight Simulator via FSUIPC 7 (free version)
Download FSUIPC 7 from the author Pete Dowson’s page
(http://www.fsuipc.com/) and run FSUIPC7.exe.
You might use FS-Interrogate from the package’s Utils folder to check FS variable offsets and value types.

## Slide 7: References and links
Arduino boards: https://www.arduino.cc/en/Main/Products
Sparkfun board used in this eyample: https://www.sparkfun.com/products/15123
Sparkfun PC drivers: https://learn.sparkfun.com/tutorials/how-to-install-ch340-drivers
Arduino programming language reference: https://www.arduino.cc/reference/en/
Python pyserial library: https://pypi.org/project/pyserial/
Python FSUIPC library: https://pypi.org/project/fsuipc/
FSUIPC: http://www.fsuipc.com/
Microsoft Flight Simulator: https://www.flightsimulator.com/